## Slide 1
FORMAL MODEL - EMBEDDED SOFTWARE - HARDWARE RTL - REQUIREMENTS
Cross Traffic
Management
A four-leg, single-lane crossroad coordinated entirely through V2I / V2V
communication - no traffic lights, no collisions.
PREPARED BY
Boiddo Sumon
Ferdous Soaib
Nnachi-Egwu Nnaemeka
Oyemade Oluwasholape Daniel
UPPAAL
Timed-automata formal model
FreeRTOS / C
IMTask + LaneTask x4 implementation
VHDL / RTL
aim_intersection_manager + testbench

## Slide 2
Project Overview
What the system is, and who it serves
The system models an cross traffic management system for a four-leg, single-lane crossroad.
Autonomous vehicles cross a shared intersection
without traffic lights, without collisions, and with minimal waiting time.
V2I (vehicle-to-infrastructure) and V2V (vehicle-to-vehicle) communication fully replace traditional signal control.
STAKEHOLDERS
Autonomous Vehicles
Cross safely and quickly
Intersection Manager
Coordinate crossing, prevent conflicts
Road Infrastructure
Provide the V2I communication point
Other Vehicles
Receive V2V awareness of active crossings
2

## Slide 3
Topology, Actors & Use Cases
Four approaches, three actors, ten coordinated use cases
N
S
E
W
4-leg intersection - single lane per approach
(German right-hand traffic)
Autonomous Vehicle (AV)
Arrive - request - receive grant/defer - broadcast intent - cross - notify exit
Intersection Manager (IM/RSU)
Check compatibility - grant or defer - update crossing state
Other Vehicles (V2V peers)
Receive crossing-intent broadcasts from active vehicles
Full use case diagram (UC1-UC10) provided in the Requirements Specification.
3

## Slide 4
Functional Requirements
What the system shall do (FR1-FR10)
FR1
Intersection topology - 4 approaches (N/S/E/W), one entry + one exit lane each
FR2
Movement types - Straight, right turn, or left turn per vehicle
FR3
V2I request - Vehicle sends direction + movement to the IM
FR4
Compatibility check - IM checks request against active crossings
FR5
Grant - IM grants when compatible; vehicle must wait for it
FR6
Defer - IM defers on conflict; vehicle waits, then retries
FR7
V2V broadcast - Vehicle broadcasts crossing intent after grant
FR8
Crossing - Vehicle crosses within the defined service time
FR9
Exit notification - Vehicle notifies IM on completion to free state
FR10
No traffic lights - All coordination via V2I reservation + V2V awareness
4

## Slide 5
Non-Functional Requirements & the M/M/2 Rule
How well the system must perform, and the compatibility rule behind it
Safety
No conflicting crossings, ever
Liveness
Every request eventually granted
Deadlock-free
IM can always respond
Bounded
Max 4 vehicles crossing at once
Throughput
M/M/2: 2 compatible streams at once
Real-time
Grant/defer decided in one step
Protocol format
Direction + movement + message type
COMPATIBILITY RULE (M/M/2)
Scenario | OK? | Reason
N-straight + S-straight | Yes | Opposite lanes, never cross
E-straight + W-straight | Yes | Opposite lanes, never cross
Any right turns together | Yes | Each stays in its own corner
N-straight + E-straight | No | Paths cross in the center
Any left turn + anything | No | Left turns sweep through center
5

## Slide 6
Cross Traffic Management - Use Case Diagram
Three actors, ten coordinated use cases - Autonomous Vehicle, Intersection Manager (RSU), and V2V peer vehicles
Cross Traffic Management System
Autonomous
Vehicle (AV)
Other Vehicles
(V2V peers)
Intersection
Manager (IM/RSU)
UC1
Arrive at intersection
UC2
Send crossing request
UC3
Receive grant
UC4
Receive defer & retry
UC5
Broadcast crossing intent (V2V)
UC6
Receive V2V intent from other car
UC7
Cross intersection
UC8
Send exit notification
UC9
Check path compatibility
UC10
Update crossing state
6

## Slide 7
UPPAAL Formal Model
Three timed-automata templates coordinated through typed channels
IM
1 instance
Ready + 4 committed Proc states; grants/defers each of 4 requesters
Car(id)
4 instances - N,S,E,W
Idle -> Queued -> WaitResp -> Deferred / V2V -> Crossing -> Idle
V2VListener(sid)
4 instances - N,S,E,W
Single Listen state; reacts to broadcast channel vv[sid]?
SHARED DECLARATIONS
int cc - crossCount (vehicles currently crossing)
int cm - crossMode (which movement class owns the intersection)
int rm[4] - requested movement per direction
chan rq[4], gr[4], df[4] - per-direction request / grant / defer
broadcast chan vv[4] - V2V crossing-intent broadcast
VERIFICATION QUERIES
Q1-Q5 formally check deadlock-freedom, path exclusivity, and the M/M/2 pairing rule - see next section.
7

## Slide 8
UPPAAL Editor — Intersection Manager (IM) Model
The real IM template: committed Proc0–Proc3 states implement the compatibility guard for each direction
IM TEMPLATE — EDITOR VIEW
Each Proc_i fires gr[i]! when compatible with the active crossing mode, or df[i]! otherwise — mirrors canGrant() in FreeRTOS and can_grant_fn() in VHDL.
Captured from UPPAAL 5.1.0-beta5 (aim_uppaal_final.xml)
8

## Slide 9
Car Protocol State Machine
Exact state flow modeled in UPPAAL and mirrored in the LaneTask retry loop
Idle
choose movement
Queued
rq[id]!
WaitResp
gr[id]? / df[id]?
V2V
vv[id]! broadcast
Crossing
d <= SERVICE
Deferred
d <= DEFER_T
defer
retry (wait elapsed)
cc==1: reset cross state to empty | cc>1: decrement
1:1 mapping to code: Idle/Queued/WaitResp/Deferred/V2V/Crossing correspond directly to the retry loop, xQueueSend/xQueueReceive calls, and vTaskDelay(SERVICE_MS) / vTaskDelay(DEFER_MS) in LaneTask() (aim_freertos.c).
9

## Slide 10
Formal Verification Results
Five UPPAAL queries check the safety-critical properties of the model
Q1
No deadlock
A[] not deadlock
The system can always make progress
Q2
Path exclusivity
N-straight & E-straight never together
Conflicting paths never overlap
Q3
M/M/2 server 1
N & S cross together only if both straight
Opposite-lane pairing enforced
Q4
M/M/2 server 2
E & W cross together only if both straight
Opposite-lane pairing enforced
Q5
Bounded crossings
cc <= 4 at all times
Never more than 4 vehicles crossing
All five properties are verified TRUE against the UPPAAL model, giving formal assurance that the same rules implemented in FreeRTOS and VHDL are safe by construction.
10

## Slide 11
UPPAAL Editor — Car Template & Verifier
Left: the full Car(id) state machine as modeled. Right: all five safety and liveness queries in the Verifier
CAR TEMPLATE — EDITOR VIEW
Idle → Queued → WaitResp → Deferred/V2V → Crossing → Idle, with d ≤ DEFER_T and d ≤ SERVICE bounding each wait.
VERIFIER — SAFETY & LIVENESS QUERIES
A[] not deadlock, path exclusivity, M/M/2 server pairing (Q3/Q4), and cc ≤ 4 — all checked against the model.
Captured from UPPAAL 5.1.0-beta5 (aim_uppaal_final.xml)
11

## Slide 12
FreeRTOS System Architecture
Direct task-for-template mapping from the UPPAAL model
IMTask
x1 - priority +3 (highest)
Reads v2i_reqQueue; runs canGrant(); sends GRANT/DEFER; handles EXIT
LaneTask
x4 - priority +1
Arrival timing; V2I request/retry loop; V2V broadcast; crossing delay
V2VListenerTask
x4 - priority +2
Subscribes to v2v_broadcastQueue[dir]; updates awareness table
QUEUES & SYNCHRONIZATION
v2i_reqQueue - all 4 lanes to IM (shared request channel)
v2i_respQueue[4] - IM to lane[dir] (GRANT / DEFER)
v2v_broadcastQueue[4] - one per sender, fan-out to listeners
imMutex, v2vMutex - protect crossCount/crossMode and awareness table
DESIGN NOTE
IMTask runs at the highest priority so it never blocks a LaneTask waiting on a grant/defer decision - directly satisfying NFR6 (real-time response): the IM always decides within one atomic step.
12

## Slide 13
V2I / V2V Protocol Flow in Code
One crossing cycle, from arrival to exit notification
1
Arrive
random inter-arrival
[2000-8000 ms]
2
Request
V2IRequest(dir,move)
via v2i_reqQueue
3
Grant / Defer
canGrant() check
responds on v2i_respQueue
4
Broadcast
V2V intent to all
other directions
5
Cross
hold intersection for
SERVICE_MS = 4000
6
Exit
v2i_exit() decrements
crossCount
On DEFER, the vehicle waits DEFER_MS = 3000 ms then re-enters step 2 (retry) - guaranteeing liveness (NFR2) without polling the IM continuously.
KEY TIMING CONSTANTS (aim_freertos.c)
Constant | Value | Meaning
MIN_ARR_MS / MAX_ARR_MS | 2000 / 8000 | Vehicle inter-arrival window
SERVICE_MS | 4000 | Time spent crossing the intersection
DEFER_MS | 3000 | Wait time before retrying after a defer
MAX_QUEUE | 6 | Max queued vehicles per approach
13

## Slide 14
Runtime Simulation — Compatible Crossings (Case 1)
FreeRTOS AIM simulator: canGrant() lets non-conflicting movements cross the intersection together
CASE 1 — N-straight + S-straight
Same mode (MODE_NS_STR) — both cars GRANTed; crossMode: NS_STRAIGHT. This is M/M/2 server 1 (opposite lanes never cross).
Captured from the FreeRTOS AIM simulator console (aim_freertos.c)
14

## Slide 15
Runtime Simulation - Compatible Crossings
FreeRTOS AIM simulator: canGrant() lets non-conflicting movements cross together
CASE 2 - E-straight + W-straight
Same mode (MODE_EW_STR) - both cars GRANTed; crossMode: EW_STRAIGHT, crossCount: 0 before entry.
CASE 3 - All Right Turns Together
MODE_RTURN allows all four corners at once - crossMode: RIGHT_TURN, crossCount: 4, all four GRANTed.
Captured from the FreeRTOS AIM simulator console (aim_freertos.c) - matches the UPPAAL canGrant() guards exactly.
15

## Slide 16
Runtime Simulation - Exclusive Left Turn & Retry
canGrant() defers conflicting cars, then grants the retry once the intersection clears
CASE 4 - Left Turn is Exclusive
N-left GRANTed alone (MODE_EXCL); S/E/W straight requests all DEFER until it exits.
AFTER EXIT - Waiting Car Retries
crossCount returns to 0 on EXIT; the deferred car retries after DEFER_MS and is GRANTed.
Demonstrates NFR2 (liveness): every deferred vehicle is eventually granted - no starvation.
16

## Slide 17
VHDL Hardware Implementation
entity aim_intersection_manager - the same rule, synthesized as RTL
KEY PORTS
clk, rst
system clock; synchronous active-high reset
v2i_req_valid[4], v2i_req_move[8]
1 bit + 2 bits/car - request + movement (00 straight, 01 right, 10 left)
v2i_grant[4], v2i_defer[4]
one-cycle pulse per car - grant or defer
v2i_exit[4]
car finished crossing
v2v_intent[4] -> v2v_aware[4]
V2V broadcast passthrough
cross_count[3], cross_mode[2]
cnt_reg (0-7) and mode_reg ("00".. "11")
can_grant_fn(dir, mv, mode_r, excl, cnt)
excl='1' -> false (exclusive left-turn active)
cnt = 0 -> true (intersection empty)
mv = LEFT -> false (left turns always exclusive)
get_mode_fn(dir,mv) = mode_r -> true
otherwise -> false (defer)
TESTBENCH - tb_aim_intersection_manager (ModelSim / Questa, 100 MHz / 10 ns clk)
T1-T2
N then S straight, empty -> both GRANT, M/M/2 server 1 (mode 01)
T3
E straight while NS active -> DEFER (cross-conflict)
T4
N & S exit -> cross_count=0, mode reset to empty
T5
N & W broadcast V2V intent -> v2v_aware reflects both
T6
All 4 right turns at once -> all GRANT, mode=11 (right-turn)
T7-T8
N left turn -> GRANT + exclusive; S straight during it -> DEFER
17

## Slide 18
M/M/2 Crossing-Mode Mapping
getMode()/canGrant() in C and can_grant_fn() in VHDL enforce the identical rule
Mode | Meaning | VHDL encoding | Compatible movements
MODE_EMPTY | Intersection idle | "00" | Any new request accepted
MODE_NS_STR (server 1) | N/S straight active | "01" | Only more N/S straight requests
MODE_EW_STR (server 2) | E/W straight active | "10" | Only more E/W straight requests
MODE_RTURN | Right turns active | "11" | All right turns, any direction
MODE_EXCL | Left turn active | excl_flag='1' | No other movement until it exits
canGrant() / can_grant_fn(): true if the intersection is empty, or the requested movement's mode matches the active mode and is shareable (right turns or the same straight server). Left turns and cross-conflicting straights are always deferred - identical logic in C and VHDL.
18

## Slide 19
Traceability: Requirement to Implementation
The same behavior, expressed three ways
Requirement | UPPAAL | freeRTOS | VHDL
FR4 - compatibility | Guards on Proc transitions | canGrant() function | can_grant_fn() in RTL
FR5/FR6 - grant/defer | gr[id]! / df[id]! | RESP_GRANT / RESP_DEFER | v2i_grant / v2i_defer pulses
FR7 - V2V broadcast | vv[id]! broadcast chan | v2v_broadcastQueue | v2v_intent input bus
NFR1 - safety | Q2 verified | canGrant() prevents conflict | can_grant_fn() hardware
NFR4 - bounded (<=4) | Q5 verified | cc<=4 max crossings | cnt_reg range 0-7
NFR5 - M/M/2 | cm modes 1 and 2 | MODE_NS_STR / MODE_EW_STR | mode_reg "01" / "10"
All three columns were independently verified: 5 UPPAAL queries, the aim_freertos.c retry/priority design, and 8 directed VHDL testbench cases (tb_aim_intersection_manager).
19

## Slide 20
System Constraints & Scope
Boundaries the design operates within (SC1-SC7)
SC1
Single-lane approaches - no dedicated turn lanes
SC2
All vehicles are V2I / V2V capable
SC3
IM is a single roadside unit (RSU)
SC4
Queuing model: M/M/2 (Markovian arrivals, exponential service, 2 servers)
SC5
Hardware implementation: VHDL (aim_intersection_manager), verified in ModelSim / Questa
SC6
Software implementation: C with FreeRTOS
SC7
Formal model: UPPAAL timed automata
20

## Slide 21
KEY TAKEAWAYS
One Rule, Three Implementations
Safety by construction
The same canGrant() compatibility rule is enforced identically in UPPAAL, C/FreeRTOS, and VHDL
Formally verified
5 UPPAAL queries confirm no deadlock, path exclusivity, correct M/M/2 pairing, and a bounded crossing count
Liveness guaranteed
The defer-and-retry loop ensures every vehicle is eventually granted - no starvation
No traffic lights needed
V2I reservation plus V2V awareness fully replace signal-phase control
Cross Traffic Management - UPPAAL x FreeRTOS x VHDL

## Slide 22
THANK YOU FOR LISTENING
QUESTIONS?