## Slide 1
IEEE TECHNICAL PAPER
Sharing and Binding
within High-Level Synthesis
Oluwasholape Oyemade
Department of Electronic Engineering · Hochschule Hamm-Lippstadt · Lippstadt, Germany
Resource Sharing
Binding Algorithms
Graph Coloring
RTL Generation

## Slide 2
Introduction
What is High-Level Synthesis?
HLS transforms a behavioral description into a hardware implementation at Register Transfer Level (RTL).
Designers work at an algorithmic level — HLS handles registers, multiplexers, and control logic.
Why Sharing & Binding?
1. Sharing reduces hardware area by reusing functional units and registers. 2. Binding is the assignment process that realizes sharing in the datapath. 3. Together they determine whether the final RTL is area-efficient or parallel.
⏱ SCHEDULING
When do operations execute?
📦 ALLOCATION
Which resource types are available?
🔗 BINDING
Which operation uses which instance?
Focus of this paper

## Slide 3
Mathematical Foundations
Data-Flow Graph (DFG)
G = (V, E)
V = operation nodes (arithmetic, logical, memory)
E = dependency edges (data flows)
Binding Function
B: O → R
Assigns each operation to a
concrete hardware resource instance
Sharing Condition
Two operations op_i and op_j may share the same resource instance if and only if:
T(op_i) ∩ T(op_j) = ∅
(execution intervals are disjoint)

## Slide 4
Resource Sharing
The reuse of hardware units across compatible operations to reduce area and improve utilization.
⚙ Functional Unit Sharing
Three additions do not require three adders. If additions execute in different clock cycles, a single adder handles all of them. Cost: multiplexers to select operands + controller activation logic.
💾 Register Sharing
Variables with non-overlapping lifetimes share one physical register. Example: x: produced cycle 1 → used cycle 3
y: produced cycle 4 → used cycle 6
Lifetimes disjoint →
1 register suffices.
⚡ Sharing reduces both arithmetic units AND storage — but poor register binding can increase multiplexing and routing cost.

## Slide 5
Binding — The Mechanism of Sharing
Binding specifies on which resource type and on which resource instance a task is implemented. It is the synthesis task that directly realizes sharing in the generated architecture. (Teich & Haubelt)
When Can Binding Occur?
Before Scheduling
Binding constraints guide the scheduler
After Scheduling
Intervals known → interval graph + LEFTEDGE
Together with Scheduling
Joint optimization, higher complexity
★ Focus of this paper
Two Levels of Binding
Resource-Type Binding — Multiplier? ALU? Memory?
Resource-Instance Binding — Multiplier 1 or 2?
Sharing occurs here ↑

## Slide 6
Graph-Theoretic Binding
Compatibility Graph
Vertices: operations Edge: two ops may share a resource Optimal binding → partition into minimum number of cliques
Conflict Graph
Vertices: operations Edge: two ops CANNOT share a resource Optimal binding → graph coloring (each color = one resource instance)
After Scheduling → Interval Graph
Each operation has interval I_i = [l_i, r_i). Two operations conflict ⟺ their intervals overlap.
The conflict graph of non-overlapping intervals forms an interval graph → colorable in polynomial time.
Compatibility types: weak · schedule · strong (this paper focuses on schedule compatibility)

## Slide 7
The LEFTEDGE Algorithm
Pseudocode
LEFTEDGE(intervals):
sort intervals by start time
color = 0
while intervals not empty:
color = color + 1
r = 0
for each interval I in order:
if start(I) >= r:
assign color to I
r = finish(I)
remove I from intervals
return colors
Properties & Significance
✓ Exact for interval graphs
Produces optimal (minimum) coloring.
⚡ O(|V| log |V|) runtime
Dominated by sorting step — highly efficient.
🏗 Design-time only
Algorithm runs during synthesis, not at runtime.
🎨 Color = Resource instance
Same color → operations share one physical unit.
Interval example: 5 ops → 2 resource instances (colors)

## Slide 8
LEFTEDGE — Worked Example
Five multiplication operations to bind onto minimum multiplier instances:
Operation
Interval
Resource
Overlaps with
Color
Mul1
[1, 3)
Multiplier
—
Color 1
Mul3
[2, 6)
Multiplier
Mul1
Color 2
Mul2
[3, 5)
Multiplier
Mul3
Color 1
Mul5
[5, 7)
Multiplier
Mul2, Mul3
Color 2
Mul4
[6, 8)
Multiplier
Mul5
Color 1
Result: 5 multiplications → 2 multiplier instances | Color 1 = Multiplier 1 · Color 2 = Multiplier 2

## Slide 9
Runtime & Hardware Overhead
Benefits of Sharing
⬇ Area
Fewer adders, multipliers, registers instantiated
⬆ Utilization
Each resource instance used by multiple operations
✓ Equivalent Behavior
RTL is functionally identical to unshared version
⚡ O(|V|log|V|)
LEFTEDGE runtime — fast at design time
Structural Overhead
⊕ Multiplexers
Needed to route correct operands to shared units
⊕ Control Logic
Controller activates resources per clock cycle
⊕ Routing Complexity
More interconnects possible with heavy sharing
⊕ Latency Trade-off
Serialized ops → longer schedule possible
Sharing is a design tradeoff — always evaluate area, latency, and control complexity together.

## Slide 10
Application: FIR Filter Example
y[n] = Σ h_i · x[n−i] for i = 0 to 3
Fully Parallel
Mul1 → Multiplier 1
Mul2 → Multiplier 2
Mul3 → Multiplier 3
Mul4 → Multiplier 4
4 multipliers · high throughput · max area
vs.
With Binding (Shared)
Mul1, Mul2 → Multiplier 1
Mul3, Mul4 → Multiplier 2
Requires: muxes to select operands
+ controller logic per cycle
2 multipliers · 50% area saving · serialized

## Slide 11
RTL Realization — Effect of Binding
Binding decisions directly shape the generated RTL netlist — altering functional units, multiplexers, registers, and control logic.
Shared Functional Units
Fewer multipliers/adders instantiated. Each handles multiple operations across time-multiplexed cycles.
Multiplexers
Added to route correct operands to each shared unit. Number of mux inputs = number of operations sharing that unit.
Registers
Store intermediate values between cycles. Register binding reduces storage elements but may affect routing.
Control Logic
FSM or controller activates the correct operation and selects operands each clock cycle based on the schedule.
A different binding → different RTL cost even for the same behavioral algorithm.

## Slide 12
Design Tradeoffs & Limitations
✓ Where Sharing Works Well
Area-constrained designs (embedded, IoT, low-cost FPGA)
Moderate throughput requirements allow serialization
Operations are already spread over many clock cycles
Scheduling intervals are fixed → LEFTEDGE is directly applicable
⚠ Limitations
Not suitable for high-parallelism or strict low-latency designs
Simultaneous operations cannot share a non-pipelined resource
Optimal resource count ≠ globally optimal timing/power/routing
Interconnect and multiplexer depth not captured by interval model alone
Design-Space Implication
More sharing → fewer resources, less parallelism. Less sharing → more parallelism, higher area cost. HLS tools explore multiple schedule-binding pairs to find the best area-performance tradeoff.

## Slide 13
CONCLUSION
Sharing and Binding in HLS
⚙
Resource sharing reuses functional units and registers across compatible operations, reducing hardware area.
🔗
Binding is the synthesis mechanism that assigns operations to resource instances, realizing sharing in the datapath.
📐
Binding-after-scheduling yields an interval graph, solvable exactly and efficiently with LEFTEDGE in O(|V|log|V|).
🏗
The FIR example demonstrates a 50% multiplier reduction, but introduces muxes, registers, and control overhead.
⚖
Effective HLS balances resource savings against latency, throughput, and implementation complexity.
Hochschule Hamm-Lippstadt · IEEE Format · Based on Teich & Haubelt (2007)